Data note for paper “Surface Coseismic Displacement and GPS-derived Seismic Ground Shaking Associated with the 2006 ML=6.96 and ML=6.99 Pingtung Earthquake Doublet, offshore Southern Taiwan” by Chen et al., 2008

1. Data sets

We utilize part of the Taiwan CORS which is a cooperative program operated by Central Weather Bureau (CWB), Ministry of Interior (MOI), Institute of Earth Sciences, Academia Sinica (IESAS), and several other Institutes and Universities.

2. Station category

CWB stations: CLON, CTOU, DAWN, FALI. HENC, JLUT, LIUC, NJOU, SGAN

MOI stations: KDNM, TMAM

IESAS stations: DONA, S01R, S103, TSHO, YENC

3. Coseismic displacement

3.1. Daily solution

Table 1. Total coseismic displacements combined two main shocks of the 2006 Pingtung earthquakes computed by daily solution.

| Stations | Latitude (°) | Longitude(°) | Height (m) | dN (mm) | dE (mm) | dh (mm) |
| --- | --- | --- | --- | --- | --- | --- |
| CLON | 22.430 | 120.579 | 49.350 | -2.0±1.1 | -2.0±1.6 | -9.7±24.6 |
| CTOU | 22.754 | 120.277 | 25.643 | -0.5±0.6 | -0.2±1.1 | -4.1±24.7 |
| DAWU | 22.340 | 120.890 | 41.023 | 1.5±0.7 | -4.3±1.3 | -10.7±25.1 |
| DONA | 22.915 | 120.703 | 522.704 | 3.0±0.8 | 0.9±0.9 | -2.6±25.4 |
| FALI | 22.365 | 120.593 | 41.708 | -4.6±0.6 | -4.3±1.2 | -12.9±27.1 |
| HENC | 22.003 | 120.746 | 46.659 | -1.7±1.1 | -48.6±2.0 | -45.4±30.4 |
| JLUT | 22.329 | 120.622 | 29.966 | -6.0±0.8 | -6.4±1.1 | -13.2±31.4 |
| KDNM | 21.949 | 120.782 | 58.297 | 3.5±1.5 | -37.7±1.6 | -30.2±32.2 |
| LIUC | 22.346 | 120.369 | 62.114 | -38.4±0.7 | -0.3±1.1 | -12.0±33.4 |
| NJOU | 22.503 | 120.571 | 52.207 | 0.4±1.0 | -0.4±1.1 | -7.1±35.3 |
| S01R | 23.655 | 119.592 | 49.835 | -0.3±0.0 | 0.6±0.1 | 0.0±37.1 |
| S103 | 23.564 | 120.475 | 125.362 | 0.0±0.5 | 1.5±1.1 | -0.1±37.2 |
| SGAN | 22.581 | 120.349 | 30.243 | -1.5±3.7 | -4.2±4.9 | -6.2±38.4 |
| TMAM | 22.616 | 121.007 | 58.744 | 2.3±0.8 | 1.1±1.2 | -3.1±42.1 |
| TSHO | 22.904 | 120.351 | 68.233 | 0.9±0.4 | 1.2±1.0 | 1.7±50.2 |
| YENC | 22.763 | 120.376 | 70.949 | -0.5±0.6 | -1.0±1.1 | -2.2±44.1 |

3.2 Kinematic postioning

Table 2. Individual coseismic displacements of two main shocks associated with the 2006 Pingtung earthquakes computed by 1 Hz data

| Stations | EQ1 (UTC: 12h 26m 21.0s) | EQ2 (UTC: 12h 34m 15.3s) |
| --- | --- | --- |
|  | dN (mm) | dE (mm) | dh (mm) | dN (mm) | dE (mm) | dh (mm) |
| CLON | -2.6±9.1 | 14.7±5.7 | 17.3±14.8 | -2.0±6.6 | -6.5±5.0 | -9.7±14.1 |
| CTOU | -12.5±8.3 | 6.9±6.2 | -0.6±15.1 | 0.3±7.6 | 0.3±6.2 | -14.0±13.2 |
| DAWU | -1.1±8.4 | 16.7±6.1 | -2.4±15.3 | 0.1±6.9 | -16.4±4.9 | 1.2±13.1 |
| DONA | -3.0±8.1 | 12.7±5.2 | 6.4±13.3 | 4.7±6.9 | -4.7±5.1 | -16.1±12.4 |
| FALI | -14.5±8.5 | 17.7±5.5 | 7.6±15.9 | 0.0±7.4 | -11.7±5.0 | 0.0±13.7 |
| HENC | -19.6±8.6 | -16.2±5.0 | -14.5±14.4 | 6.3±8.1 | -23.8±5.3 | 4.3±13.3 |
| JLUT | -8.4±8.3 | 16.0±6.0 | 28.6±16.5 | -9.4±7.4 | -16.0±5.7 | -19.8±15.7 |
| KDNM | -8.5±5.1 | -5.2±5.1 | 1.6±10.6 | 14.3±7.5 | -19.3±6.8 | 6.3±14.2 |
| LIUC | -15.2±9.1 | -1.2±5.7 | 6.3±13.7 | -28.3±8.6 | 1.5±6.8 | -25.4±13.1 |
| NJOU | -12.5±9.2 | 17.9±4.9 | -7.6±12.0 | -0.8±7.1 | -4.0±5.8 | 5.2±13.3 |
| S01R | -9.0±10.4 | 5.3±3.9 | 10.8±13.7 | -3.2±6.1 | 0.2±4.0 | -13.5±12.7 |
| S103 | 1.1±7.6 | 4.9±4.1 | 1.1±11.9 | 4.7±6.7 | 0.3±4.3 | 4.7±12.4 |
| SGAN | -5.6±7.6 | 15.0±5.2 | 32.3±15.3 | 6.1±7.1 | -0.2±5.9 | -13.7±14.7 |
| TMAM | -1.8±7.5 | 17.5±4.3 | 2.0±12.6 | 6.5±6.4 | -3.5±4.5 | 13.2±12.3 |
| TSHO | -8.8±9.1 | 5.2±5.7 | -4.0±16.7 | -0.8±8.8 | 0.4±5.9 | -10.4±16.1 |
| YENC | -14.5±8.6 | 6.8±6.0 | -5.3±15.1 | 5.1±7.4 | 1.7±5.4 | 2.1±13.5 |

4. Kinematic positioning

4.1 HENC (text file see attachment ”henc.txt” )

Figure 1. 1Hz GPS data by kinematic positioning algorithm at station HENC

4.2 KDNM (text file see attachment ”kdnm.txt” )

Figure 2. 1Hz GPS data by kinematic positioning algorithm at station KDNM